## Slide 1: MODULE 1: OVERVIEW OF THE ENVIRONMENTAL AND SOCIAL IMPACT ASSESSMENT (ESIA) PROCESS IN NIGERIA AND THE WORLD BANK
SUSTAINABLE PROCUREMENT ENVIRONMENT AND SOCIAL STADARDS CENTRE OF EXCELLENCE
Ahmadu Bello University, Zaria.
EXECUTIVE SHORT-TERM COURSES
IN
ENVIRONMENTAL STANDARDS
A 5- day course for earning a certificate of attendance for ESA Practitioners
Topic: The National Guidelines and Standards for Pollution Control in Nigeria of 1991
Lecturer – Dr I. Mukhtar

## Slide 2: INTRODUCTION
Industrialization is vital to a nation's socio-economic development as well as its political stature in the international committee of nations. It provides ready employment opportunities for a good percentage of the population in medium to highly developed economies.
However, industries vary according to process technology, size, nature of products, characteristics and complexity of wastes discharged.

## Slide 3
Ideally, siting of industries should strike a balance between socio-economic and environmental considerations
. Availability and access to raw materials, Proximity of water sources market for products, cost of effective transportation route, major settlements and labour as well as infrastructural amenities often influence the siting of industries

## Slide 4
Rapid industrial development in developed and developing countries have increased hazardous wastes generation several fold
Realising the low-level of environmental awareness in developing countries, coupled with the non-existence of environmental protection laws, and the abject poverty of these nations, the developed countries have, within the last decade, embarked upon "Toxic Wastes Trade" or "Illegal Dumping of Toxic Wastes" in poor, debt-strapped developing countries.

## Slide 5
Nigeria has been a victim of this illegal act, when in 1988 about 3,880 tons of toxic and hazardous wastes were dumped in Koko, Bendel State by an Italian Company.
Guidelines and standards relate to six areas of environmental pollution control were issued by the Federal Environmental Protection Agency (FEPA). These guidelines and standards relate to six (6) areas of environmental pollution control: (i)Effluent limitations (ii) Water quality for industrial water uses at point of in-take (iii) Industrial emission limitations (iv) Noise exposure limitations (v) Management of solid and hazardous wastes (vi) Pollution abatement in industries.

## Slide 6: EFFLUENT LIMITATION GUIDELINES
(i) Metal and Mining
(ii) Food, Beverages and Tobacco
(iii) Breweries, Distilleries and Blending or Spirits
(iv) Textiles
(v) Tannery
(vi) Leather products
(vii) Woods, Wood products including furniture and fixtures
(viii) Pulp, Paper and paper products
(ix) Chemical and Allied
(x) Others

## Slide 7: WATER QUALITY STANDARDS
Water quality requirements differ for various industries and processes even within the same plant. Water treatment technology is often employed to bring raw process water to the desired quality for each industry.
It is important that industries monitor their effluents in-house while FEPA will also cross-check the effluent characteristics to ascertain the degree of compliance with the proposed guidelines.

## Slide 8: GASEOUS EMISSION AND AMBIENT AIR QUALITY LIMITATIONS
Guidelines for emission limits from stationary sources represent maximum allowable levels of pollutants from a site, process, stack, vent, etc. with the objective of achieving a desired air quality. The prescribed emission limits depend on socio-economic and political considerations.

## Slide 9: NOISE EXPOSURE LIMITS FOR NIGERIA
Industrial or workplace noise arises from occupational exposure of workers to noise from industrial machines or exposure of neighbourhood population to noise from factories nearby. This is quite important in the country as most industrial estates exist alongside or close to residential areas.
Exposure to industrial and other forms of noise can induce hearing loss and other pathological changes in the affected population.
Hence, it is recommended that daily noise exposure for workers should not exceed 90 decibels, dB(A) daily for a 8-hour working period.

## Slide 10: GUIDELINES FOR THE MANAGEMENT OF SOLID AND HAZARDOUS WASTES
(a) maintain an up-to-date register of toxic, hazardous and radioactive substances;
(b) control the generation of toxic, hazardous and radioactive wastes and ensure that those banned shall be stringently controlled;
(c) monitor the effects and control all phases of the life-cycle of all substances likely to have an adverse impact on human health and environment;

## Slide 11
(d) determine and use environmentally safe and technologically sound techniques for disposal of toxic, hazardous and radioactive wastes;
(e) set up regional framework and standards for the proposed "DUMP WATCH" against trans-boundary movement of toxic, hazardous and radioactive wastes and for the achievement of the environmentally sound management of hazardous substances.

## Slide 12: SPILLS AND DISCHARGES INTO THE ENVIRONMENT
This section sets out the requirement for any person responsible for a spill or discharge into the environment except when such release is otherwise permitted under the provision of "FEPA Guideline".
For the purposes of complying with this section, a transporter who spills or discharges dangerous waste or hazardous substance during transportation will be considered the responsible person.

## Slide 13: CONCLUSION
This guideline shall be applied when any dangerous waste or hazardous substance is intentionally or accidentally spilled or discharged into the environment (unless otherwise permitted) such that public health or environment are threatened, regardless of the quantity of dangerous waste or hazardous substance

## Slide 14
THANK YOU