## Slide 1: The National Effluents Limitations Regulation
By
Prof. Wisdom Sohunago Japhet
PhD (Ecology) NENU CHINA

## Slide 2
Consists of a set of guidelines for the discharge/treatment of effluents emanating from industries.
There are three schedules in this instrument

## Slide 3
The First Schedule describes the important waste water parameters for 23 industrial classifications such as Aluminum industry, Sugar Cane; Fertilizers, Cement, inorganic Chemicals, Leather Tanning, Petroleum refining, e.t.c.
The Second Schedule provides Effluent limitation guidelines in Nigeria for all categories of industries
The third Schedule provides National , Effluent Limitations and Gaseous Emissions Guidelines in Nigeria for Specific Industries

## Slide 4: Installation of anti‐pollution equipment
(1) Every industry shall install anti‐pollution equipment for the detoxification of effluent and chemical discharges emanating from the industry.
(2) An installation made pursuant to paragraph (1) of this regulation shall be based on the Best Available Technology (BAT),the Best Practical Technology (BPT) or the Uniform Effluent Standards (UES).

## Slide 5: Waste water parameters
(1) The selected waste water parameters for the industries specified in column 1 of the First Schedule to these
Regulations are set out in columns 2 and 3 respectively of the Schedule.
(2) The parameters shall be continuously monitored to ensure compliance with these Regulations.

## Slide 6: Treatment of effluent
(1) An industry which discharges effluent shall treat the effluent to a uniform level as specified in the Second
Schedule to these Regulations to ensure assimilation by the receiving water into which the effluent is discharged.
[Second Schedule.]
(2) The nearest office of the Federal Environmental Protection Agency shall be furnished from time to time with
the composition of any effluent treated as specified in paragraph (1) of this regulation.

## Slide 7: Additional sectorial effluent limitation treatment
An industry specified in column 1 of the Third Schedule to these Regulations shall be subject to the additional
sectoral effluent limitations set out in columns 2 and 3 respectively of the Schedule.

## Slide 8: Penalty
A person who contravenes a provision of these Regulations is guilty of an offence and liable on conviction to the
penalty specified in section 36 or 37 of the Federal Environmental Protection Agency Act.

## Slide 9: Short title
These Regulations may be cited as the National Environmental (Effluent Limitation) Regulations.

## Slide 10: Regulatory authorities
• National Environmental Standards and Regulations Enforcement Agency (NESREA).
• National Oil Spill Detection and Response Agency.
• Federal Ministry of Environment.
• Directorate of Petroleum Resources (DPR).
• Nigerian Nuclear Regulatory Authority.
• Federal Ministry of Water Resources
• National Oil spill Detection and Response Agency (NOSDRA)
• National Biosafety Management Agency
• Department of Climate Change
• Energy Commission of Nigeria
• Erosion, Floods and Coastal Zone Management
• Department of Planning, Research and Statistics
• Drought and Desertification Agency