## Slide 1: The Environmental and Social Impact Assessment (ESIA) Process
By
W.S. Japhet
Programme Leader (Environmental Standards)
SPESSECE, ABU Zaria

## Slide 2: Learning objectives
Be familiar with process of ESIA
Be familiar with Risk classification
Be familiar with project categorization
Be familiar with the WB ESF and their relevance in the ESIA process

## Slide 3: Delivery mode
Classroom interactions
Overnight assignments
Discussion of case studies

## Slide 4: What is Environmental and Social Impact Assessment?
Essentially, environmental and social impact assessment (ESIA) is an environmental decision support tool, which provides information on the likely impacts of development projects to those who make the decision as to whether the project should be authorized.
The purpose of an ESIA is to determine the potential environmental, social, and health effects of a proposed development so that those who make the decisions in developing the project and in authorizing the project are informed about the likely consequences of their decisions before they take those decisions and are thereby more accountable.
It is intended to facilitate informed and transparent decision-making while seeking to avoid, reduce, or mitigate potential adverse impacts through the consideration of alternative options, sites, or processes.

## Slide 5: When is ESIA Required?
EIA is required for new development projects that have been identified as likely to have a significant negative impact on the environment. It is carried out before the construction phase of the project commences.
Main Objective of ESIA
The main objective of EIA is to provide decision-makers with an account of the implications of proposed courses of action before a decision on a project is made.
Legal Framework
The legal framework for conducting EIA in Nigeria is the Environmental Impact Assessment (EIA) Act CAP EI2 LFN 2004.

## Slide 6: Classifications of Risk
High Risk:
the project is likely to generate a wide range of significant adverse risks and impacts on human populations or the environment. This could be because of the complex nature of the project, the scale(large to very large) or the sensitivity of the location(s) of the project. This would take into account whether the potential risks and impacts associated with the project have the majority, any, some, or all of the following characteristics:
long term, permanent and/or irreversible (e.g. loss of major natural habitat or conversion of wetland), and impossible to avoid entirely due to the nature of the project
high in magnitude and/or in spatial extent (the geographical area or size of the population likely to be affected is large to very large)
cumulative and/or trans-boundary in nature
probability of serious adverse effects to human health and/or the environment (e.g. due to accidents, toxic waste disposal, etc.)

## Slide 7
(ii) the area likely to be affected is of high value and sensitivity, for example sensitive and valuable ecosystems and habitats (protected areas, National Parks, World Heritage Sites, Important Bird Areas), lands or rights of indigenous people or other vulnerable minorities, intensive or complex involuntary resettlement or land acquisition, impacts on cultural heritage or densely populated urban areas
(iii) some of the significant adverse environmental and social risk and impacts of the project cannot be mitigated or specific mitigation measures require complex and/or unproven mitigation, compensatory measures or technology, or sophisticated social analysis and implementation;
(iv) there are concerns that the adverse social impacts of the project, including the risk of political capture of project benefits, and the associated mitigation measures, may give rise to significant social conflicts

## Slide 8
(v) there is a history of unrest in the area of the project or the sector, and there may be significant concerns regarding the activities of security or other armed forces;
(vi) the project is being developed in a legal or regulatory environment where there is significant uncertainty or conflict as to jurisdiction of competing agencies, or where the legislation or regulations do not adequately address the risks and impacts of complex projects or changes to applicable legislation are being made, or enforcement is weak;
(vii) the past experience of the Borrower and/or the implementing agencies in developing complex projects project is limited, and their track record regarding environmental and social issues generally is poor;
(viii) Stakeholder engagement, especially community participation in the project area, is weak;
(ix) there are a number of factors outside the control of the project which could have a significant impact on the environmental and social performance and outcomes of the project.

## Slide 9: Substantial Risk
Classification of a project as Substantial Risk would include consideration of all range of relevant issues (including those identified under High Risk above) and an evaluation of how these issues, when considered together, could impact the environmental and social performance of the project. Specifically:
(i) the project may not be as complex as High Risk projects, its scale may be smaller (large to medium) and the location may not be in such a sensitive area. This would take into account whether the potential risks and impacts have the majority, any, some or all of the following characteristics:
 mostly temporary, predictable and/or reversible, and the nature of the project does not preclude the possibility of avoiding or reversing them (although substantial investment and time may be required);
 medium in magnitude and/or in spatial extent (the geographical area and size of the population likely to be affected are medium to large);

## Slide 10
 the potential for cumulative and/or trans-boundary impacts may exist, but they are less severe and more readily avoided or mitigated than for High Risk projects;
 medium to low probability of serious adverse effects to human health and/or the environment (e.g. due to accidents, toxic waste disposal, etc.), and there are known and reliable mechanisms available to prevent or minimize such incidents;
(ii) the effects of the project on areas of high values or sensitivity will be lower than High Risk projects;
(iii) mitigatory and/or compensatory measures that may be designed more readily and be more reliable than those of High Risk projects.

## Slide 11: Moderate Risk
Classification of a project as Moderate Risk would include consideration of a range of relevant issues (including those identified under High or Substantial Risk above) and an evaluation of how these issues when considered together, could impact the environmental and social performance of the project.
(i) the potential adverse risks and impacts on human populations and/or the environment are not likely to be significant. This is so because the project is not complex and/or large, does not involve activities that have a high potential for harming people or the environment, and is located away from environmentally or socially sensitive areas. As such the impacts are likely to have the following characteristics:

## Slide 12
- predictable and expected to be temporary and/or reversible;
- low in magnitude;
- site-specific, without likelihood of impacts beyond the actual footprint of the project;
- low probability of serious adverse effects to human health and/or the environment (e.g. do not involve use or disposal of toxic materials, routine safety precautions are expected to be sufficient to prevent accidents, etc.); and
(ii) risks and impacts can be easily mitigated in a predictable manner.

## Slide 13: Low Risk
A project will be classified as Low Risk if its potential adverse risks and impacts and issues on human populations and/or environment are likely to be minimal or negligible and are less than those in projects classified as Moderate Risk.
These projects, with few or no adverse risks and impacts and issues, will not require any further environmental assessment

## Slide 14: Project categorizations
Category A: A proposed project is classified as Category A if it is likely to have significant adverse environmental impacts that are sensitive, diverse, or unprecedented.
These impacts may affect an area broader than the sites or facilities subject to physical works. EA for a Category A project examines the project's potential negative and positive environmental impacts, compares them with those of feasible alternatives (including the "without project" situation), and recommends any measures needed to prevent, minimize, mitigate, or compensate for adverse impacts and improve environmental performance.
For a Category A project, the borrower is responsible for preparing a report, normally an Environmental Impact Assessment (EIA) (or a suitably comprehensive regional or sectoral EA) that includes, as necessary, elements of the other instruments referred to in paragraph 7 of Operational Policy 4.01.

## Slide 15
Category B: A proposed project is classified as Category B if its potential adverse environmental impacts on human populations or environmentally important areas—including wetlands, forests, grasslands, and other natural habitats—are less adverse than those of Category A projects.
These impacts are site-specific; few if any of them are irreversible; and in most cases mitigatory measures can be designed more readily than for Category A projects.
The scope of EA for a Category B project may vary from project to project, but it is narrower than that of Category A EA. Like Category A EA, it examines the project's potential negative and positive environmental impacts and recommends any measures needed to prevent, minimize, mitigate, or compensate for adverse impacts and improve environmental performance.

## Slide 16
Category C: A proposed project is classified as Category C if it is likely to have minimal or no adverse environmental impacts. Beyond screening, no further EA action is required for a Category C project.
Category FI: A proposed project is classified as Category FI if it involves investment of Bank funds through a financial intermediary, in subprojects that may result in adverse environmental impacts

## Slide 17: Main Stages in the EIA Process
Screening: this is undertaken to decide which projects should be subjected to environmental assessment. The criteria used include threshold, size of projects, and sensitivity of the environment;
Scoping: The purpose of scoping is to focus on the environmental impact issues to ensure that useful and relevant results will be obtained and to determine the parameters and boundaries of the assessment. The geographical area to be covered by the EIA may need to be much greater than just the local area in which the project is to be located.

## Slide 18
Baseline study: A baseline study is essential in order to be able to determine the level of impact expected and to enable the monitoring of impacts after the development has occurred. In some cases, baseline information will need to be gathered in the field, and in others, it will already be available and need only be collated. Where a project has a number of alternative sites, each of the sites should undergo a baseline study so that the relative severity of the impacts for each alternative can be assessed.
Impact prediction: After establishing the range of impacts associated with a development, it is necessary to predict their magnitude. Here baseline studies are used to establish environmental condition levels prior to the project, forecasting methods to predict future conditions with and without the project, and comparison with environmental standards and guidelines where appropriate. Physico-chemical impacts like noise, air, and water quality using quantitative modeling procedures are well established, other impacts like socio/economic are more subjective.

## Slide 19
Impact Assessment: This follows from prediction and involves an assessment of the relative significance of the impacts when compared with regulatory requirements. Significance is a function both of the magnitude of the predicted impact but also of the sensitivity of the receiving environment (which may also depend on the geographical scale being considered, the frequency or duration of the impact, etc).
Mitigation: Mitigation involves taking measures to reduce or remove identified impacts and, if possible remedy significant adverse effects using for example:
 The control of solid and liquid wastes by recycling on site
 Minimal use of toxic substances to avoid impacts on local Ecosystems
 Sensitive design structures

## Slide 20
Review: EIA Draft report from the process is subjected to review. The proponent submits a draft EIA report which shall be evaluated by the EA Department to establish the form of review. This may include In-house Review, Panel Review, and Public Review. for the public review, a public display and review of documents for a period of 21 working days are required. Venues of the display will include, among others, the LGA, the state EPA and the Federal Ministry of Environment Headquarters.
The public shall be invited to participate in the review process through newspaper advertisements. The Final EIA report must include all issues raised at the review process and answers preferred to them by the proponent, including any amendments to the report of the EIA study.
Public involvement is now a legal requirement for EIA in Nigeria, and banks are encouraged to do so before loans are granted.

## Slide 21
Provisional Approval: The review committee assesses the report and decides if the project could proceed, or that it could go on with a few corrections, or totally repeated.
If it meets the requirement to proceed, the Federal Ministry of Environment furnishes the proponent with the reviewed report and provisional approval. The approval or disapproval of the EIA of the product by the Ministry is based on the recommendations of the independent panel of experts.

## Slide 22
Impact Mitigation Monitoring (IMM): IMM is carried out on the project by the Ministry in collaboration with State Ministries of Environment and Local Governments to ensure the implementation of:
Conditions of approval
Implementation of mitigation measure
Environmental Management Plan (EMP)

## Slide 23
Final Approval of EIA report: The final report is submitted by the proponent to the ministry. The EA department ensures that all corrections have been implemented and the report represents the position of the review committee. Approval is granted and EIA certificate and Environmental Impact Statement (EIS) is issued.
Post Decision Monitoring and Auditing: This is one of the best means of converting EIA from static to an interactive process, characterized by feedback and adjustment. The regulating body does this. This is done together with the proponents periodically during the construction and post-construction stage of the project.

## Slide 25: The World Bank Environmental and Social Framework
Introduction
On August 4, 2016, the World Bank’s Board of Executive Directors approved the Environmental and Social Framework (ESF) to help protect people and the environment in the investment projects it finances.
The ESF was launched on October 1, 2018.

## Slide 26
The ESF consists of the 10 Environmental and Social Standards (ESS), which set out the mandatory requirements that apply to Borrowers to address environmental and social risks and impacts in investment projects.

## Slide 27: ESS1:Assessment and Management of Environmental and Social Risks and Impacts
Objectives:
Identify, assess, evaluate, and manage environment and social risks and impacts in a manner consistent with the ESF
Adopt a mitigation hierarchy
Adopt differential measures so that adverse impacts do not fall disproportionately on the disadvantaged or vulnerable, and they are not disadvantaged in sharing development benefits and opportunities.
Utilize national environmental and social institutions, systems, laws, regulations and procedures where appropriate
Promote improved environmental and social performance, in ways which recognize and enhance Government capacity.

## Slide 28: ESS2:Labour and Working Conditions
Objectives:
Promote safety and health at work
Promote the fair treatment, non-discrimination, and equal opportunity of project workers.
Protect project workers, with particular emphasis on vulnerable workers
Prevent the use of all forms of forced labor and child labor
Support the principles of freedom of association and collective bargaining of project workers in a manner consistent with national law

## Slide 29: ESS3:Resource Use Efficiency and Pollution Prevention and Management
Objectives
Promote the sustainable use of resources, including energy, water, and raw materials
Avoid or minimize adverse impacts on human health and the environment caused by pollution from project activities
Avoid or minimize generations of hazardous and non-hazardous waste
Minimize and manage the risks and impacts associated with pesticide use

## Slide 30: ESS4:Community Health and Safety
Objectives:
Anticipate or avoid adverse impacts on the health and safety of project-affected communities during project life-cycle from routine and non-routine circumstances
Promote quality, safety, and climate change considerations in infrastructure design and construction, including dams
Avoid or minimize community exposure to project-related traffic and road safety risks, diseases and hazardous materials
Have in place effective measures to address emergency events
Ensure that safeguarding of personnel and property is carried out in a manner that avoids or minimizes risks to the project-affected communities

## Slide 31: ESS5:Land Acquisition, Restrictions on Land use and Involuntary Resettlement
Objectives:
Avoid or minimize involuntary resettlement by exploring project design alternatives
Avoid forced eviction
Mitigate unavoidable adverse impacts from land acquisition or restrictions on land use by providing timely compensation at replacement cost,
Assisting displaced persons in their efforts to improve, or at least restore, livelihoods and living standards to pre-displacement levels or to levels prevailing prior to the beginning of project implementation, whichever is higher
Improve living conditions of poor or vulnerable persons who are physically dis[placed, through provision of adequate housing, access to services and facilities, and security of tenure
Conceive and execute resettlement activities as sustainable development programs
Ensure that resettlement activities are planned and implemented with appropriate disclosure of information, meaningful consultation and informed participation.

## Slide 32: ESS6:Biodiversity, Conservation and Sustainable Management of Living Natural Resources
Objectives:
Protect and conserve biodiversity and habitats
Apply the mitigation hierarchy and the precautionary approach in the design and implementation of projects that could have an impact on biodiversity
Promote the sustainable management of living natural resources
Support livelihoods of local communities, including indigenous peoples, and inclusive economic development, through the adoption of practices that integrate conservation needs and development priorities.

## Slide 33: ESS7:Indigenous people/Sub-Saharan African, Historically underserved Traditional Local Communities
Objectives:
Ensure that the development process fosters full respect for affected parties’ human rights, dignity, aspirations, identity, culture, and natural resource-based livelihoods
Promote sustainable development benefits and opportunities in a manner that is accessible, culturally appropriate and inclusive
Improve project design and promote local support by establishing and maintaining an ongoing relationship based on meaningful consultation with affected parties
Obtain the Free, Prior, and Informed Consent(FPIC) of affected parties in three circumstances
Recognize, respect and preserve the culture, knowledge, and practices of Indigenous Peoples, and to provide them with an opportunity to adapt to changing conditions in a manner and in a timeframe acceptable to them

## Slide 34: ESS8:Cultural Heritage
Objectives:
Protect cultural heritage from the adverse impacts of project activities and support its preservation
Address cultural heritage as an integral aspect of sustainable development
Promote meaningful consultation with stakeholders regarding cultural heritage
Promote the equitable sharing of benefits from the use of cultural heritage

## Slide 35: ESS9:Financial Intermediaries
Objectives:
Sets out how Financial Intermediaries(FI) will assess and manage environmental and social risks and impacts associated with the subprojects it finances
Promote good environmental and social management practices in the subprojects the FI finances
Promote good environmental and sound human resources management within the FI

## Slide 36: ESS10:Stakeholder Engagement and Information Disclosure
Objectives
Establish a systematic approach to stakeholder engagement that helps Governments identify stakeholders and maintain a constructive relationship with them
Assess stakeholder interest and support for the project and enable stakeholders’ views to be taken into account in project design
Promote and provide means for effective and inclusive engagement with project-affected parties throughout the project life-cycle
Ensure that appropriate project information is disclosed to stakeholders in a timely, understandable, accessible and appropriate manner.

## Slide 37
THANKS FOR LISTENING
QUESTIONS AND COMMENTS/INPUTS?
DISCUSSION OF CASE STUDIES