## Slide 1: SUSTAINABLE PROCUREMENT, ENVIRONMENT AND SOCIAL STANDARDS ENHANCEMENT – (SPESSE) Ahmadu bello university zaria
REVIEW OF THE WORLD BANK ESMP/ESIA QUALITY AND DEVELOPMENT OF TERMS OF REFERENCE (TOR)
PROFESSOR E. M. SHAIBU-IMODAGBE

## Slide 2: TERMS OF REFERENCE [TOR]
The Government of Samanzoo desire to undertake a World Bank funding facility to provide Domestic Water Supply through a dam project of River Samandoza. To access the World Bank financial facility, the country is expected to accompany the request with an appropriately undertaken and written Environmental and Social Impact and Risk Assessment of the project.
Design an acceptable Terms of Reference for the Environmental and Social Impact and Risk Assessment of the Project

## Slide 3: Duties of the chosen consultant [Contractor] - terms of reference
The Consultant is expected to undertake detailed field and laboratory assessment and produce and ASIA Report that adequately fulfills the required conditions required by the World Bank to qualify for accessing the financial facility attached to supporting the water Supply project by submitting an ESIA with the following chapters and consisting these details for each of the chapters:
1. Methodology: State categorically the methodology used for the field investigations and the standard methods used for Laboratory studies
Providing the Basic Information of the Project including Name of the project , Country where the project is to be located, Name of the executing agency /PIU, Name of consulting firm or individual consultants undertaking the ESIA or ESMP report, Date of the start of the preparation of the ESIA or ESMP report , Date that the ESIA or ESMP report was completed.
Ensure the ESIA or ESMP report comply with the Terms of Reference for the Assignment
Ensure the ESIA report complies with the Environment and Social Standard (ESS) of the Environment and Social Framework (ESF)
1.2.1 ESS 1: Assessment and Management of Environmental and Social Risks and Impacts; Use Criteria for assessing risks and impacts, Use of the mitigation hierarchy, development of environment and social commitment plan assessment and management of Social Risks and Impacts
1.2.2 ESS 2: Labor and Working Conditions: Review and Understand clearly the terms and conditions of employment, non discrimination and equal opportunity, grievance mechanism, occupation health and safety requirements
1.2.3 ESS 3: Resource Efficiency and Pollution Prevention and Management. Undertake and Assessment of Resource efficiency of water, energy, raw materials, management of air pollution, hazardous and non hazardous waste, preparation of integrated pest management plan (if appropriate) in the Resource Efficiency and Pollution Prevention and management
1.2.4: ESS 4: Community Health and Safety. Evaluate the Safety of infrastructure, services, traffic and road and hazardous materials; ecosystem services;, emergency response and preparedness security of personnel, safety of dams ( if appropriate) for Community Health and Safety Assessment.

## Slide 4
1.2.5 ESS5 Land Acquisition, Restrictions on Land Use and Involuntary Resettlement. Assess the Project Lande requirement and acquisition and estimate if any displacement, any Resettlement, and Determine the Resettlement Action Plan (RAP) or abbreviated RAP including grievance mechanism , process framework ( if appropriate)
1.2.6 ESS6 Biodiversity Conservation and Sustainable Management of Living Natural Resources. Undertake ecosystem management plan, sustainable management of living conditions to assess Biodiversity status, Conservation and Management
1.2.7 ESS 7 Indigenous Peoples/Sub-Saharan African Historically Underserved Traditional Local Community: Identify if any any Indegenous people likely to benefit or affected by the project and obtain their Free, prior and informed consent;
1.2.8 ESS 8 Cultural Heritage; Establish and Document all Chance Find Procedures, of all legally protected cultural heritage plan
1.2.9 ESS 9: Financial Intermediaries. Establish Environment and Social Management Systems (ESMS), stakeholders engagements undertaken durng the field investigations
ESS 10: Stakeholder Engagement and Information Disclosure. Establish and register all Stakeholder Engagement Plans, meaningful consultation and information disclosure, Grievance Mechanism
1.3 Include the justification for triggering the ESSs and their compliance requirements
Clearly explain the methodology used in the ESIA/ESMP
INTRODUCTION CONT’D

## Slide 5
2. Legal and Institutional Framework
2.1 Ensure and document the relevant international treaties, conventions and agreements, national laws and regulations relating to biophysical, social and health issues been listed with reference to where and how these obligations have been met on this project?
2.2 Document the relevant institutions ( public and private) being listed with their respective roles and responsibilities towards the Project
2.3 Ensure that the relevant standards and guidelines for compliance been listed including those relating to biophysical, social and health issues?
2.4 Identified any gaps between National Systems and the ESSs and Identify all the proposed gap filling measures?

## Slide 6
3.1 Explain the land ownership structure of the local Community
3.2 Provide a Deatailed description of the different interests in land holdings which can be different from land ownership status?
3.3 Decribe the project objectives and all the project components
3.4 Define delineat the associated facilities as defined in the ESF
3.5 Describe the technologies to be used, with a motivation as to how they comply with climate change mitigations?
3.6 Clearly Explain the project timetable been clearly set out for each project phase: construction, operation, decommissioning and closure?
3.7 Present and Describe i)project design and technical drawings (ii) materials to be used during the different phases have been presented and discussed? (iii) labor requirements and management plans have been presented?
3. Project Description

## Slide 7
4.1 Sufficiently describe the associated facilities defined and their impacts on the Project or by the Project for the prediction of impacts ??
4.2 Describe the project alternatives considered in the ESIA from the technical , financial, economic, socio-cultural and low carbon emissions aspects
4.3 Ensure Comprehensive description of all the alternatives of the Project including the no go option (no project), have their main environmental, social and health impacts been compared clearly and objectively with those of the proposed project?
4. Associated Facilities and Project Alternatives

## Slide 8
TEA BREAK

## Slide 9
5.1 Identify and Describe the Environment components likely to be affected by the project sufficiently for the prediction of impacts? Including the climate; the geology, the soils, the surface hydrology; the groundwater aquifers; the air quality ( indoor and outdoor) and terrestrial and aquatic ecology?
5.2 Identify Sufficiently the social components of the environment likely to be affected by the project for the prediction of impacts?
5.3 Sufficiently Identify and describe the Current status and drivers of health (communicable and non-communicable diseases, vector-borne diseases, existing pollution-induced diseases, injuries and accidents)
5.4 Identify and Describe Sufficiently the cultural components of the environment likely to be affected by the project for the prediction of impacts?
5. Description of the Environmental and Social Baseline

## Slide 10
6.1 Clearly Explain the direct and indirect/ secondary effects of pre-construction, constructing, operating and, where relevant, after use or decommissioning of the project (including both positive and negative effects)?
6.2 Investigate the types of impacts and risks at different phases of the project, in so far as they affect the following biological, physical, health and safety and social systems? namely air quality; surface water resources; groundwater resources; soils, vegetation; biodiversity; cultural heritage; people and communities; health and safety
6.3 Consider in Details the transboundary impacts
6.4 Consider in Details also the cumulative impacts of the Project?
6.5 Consider in details the global impacts of the Project
6. IMPACTS and RISKS IDENTIFICATION (ctd)

## Slide 11
6.6 Describe All the impacts and risks in terms of the nature and magnitude of the change occurring and the nature (location, number, value, sensitivity) of the affected receptors
6.7 Predict the timescale over which the effects will occur such that it is clear whether impacts and risks are short, medium or long term, temporary or permanent, reversible or irreversible
6.8 Express in Quantitative terms as much as possible, predictions of impacts and risks, Otherwise, have qualitative descriptions been defined?
6.9 Describe the methods to predict the nature, size and scale of impacts and risks and show their appropriateness to the importance of each projected impact
6.10 Ensure that the information obtained in your project Assessment include a clear indication of which impacts and/or risks may be significant and which may not
6. IMPACTS and RISKS IDENTIFICATION (ctd)

## Slide 12
7. Environment and Social Management Plan (ESMP)
7.1 Identify and Summarize all anticipated adverse environmental and social impacts and risks in a form of a table consisting of significant environment/issues, its adverse impacts, its adverse risks, the mitigating measures, the agencies responsible for the mitigation, the time line, and the estimate of each of the measures
7.2 Identify and Summarize all monitoring measures in a form of a table with the following sequence: the mitigation measures , parameters to be measured, the method used, the frequency of measurements, the agency responsible for the monitoring , and the associated cost for each monitoring measure.
7.3 Document and Summarize all institutional arrangement, capacity development and training developed which include which party/agency is responsible for the mitigation and monitoring measures; and the training required to support the implementation and mitigation measures ?
7.4 Prepare Showing an implementation schedule and cost estimates prepared showing phases and coordination with overall project implementation plans; and (b) the capital and recurrent cost estimates and sources of funds for implementing the ESMP? Were These figures also integrated into the total project cost tables.

## Slide 13
8. Public participation and Stakeholder Engagement
8.1 Make a genuine attempt in accordance with ESS10, to consult during the ESIA process, with the public, relevant public agencies, project affected people and households, local NGOs and the media and special interest groups where applicable. Lists the groups approached and the summary of the consultations
8.2 Document and Describe the comments/recommendations made during the consultation taken into the consideration in the design and for the implementation of the project
8.3 Prepare a Stakeholder Engagement Plan
8.3 Provide a Grievance Redress mechanism
8.4. Ensure full Disclosure of the ESIA or ESMP nationally and at the location of the Project

## Slide 14
9. Environment and Social Commitment Plan (ESCP) and 10 Non Technical Summary
Environment and Social Commitment Plan
9.1 Prepare a draft ESCP for the Borrower or the Proponent of the Project
9.2 Include all Commitments in the ESCP of the Borrower/Proponent for all the ESSs triggered by the Project with a realistic time table
10 Non Technical Summary
10.1 The non-technical summary must be easily be understood by a lay-person And translated in a local language to the extent feasible or required by national laws
10.2 The ESIA / ESMP Report summary shall contain a brief but concise description of the project and the environment and social context, an account of the main environment and social issues, the ESMP and the consultation process
10.3 The summary must indicate whether the project is or is not environmentally and socially acceptable?

## Slide 15
10. Lay out
10.1 Arrange all the information logically in sections and chapters and indexed in the table of contents
10.2 Include in the report definition of terms, list of acronyms and meanings
10.3 Include in the report or appendices the Terms of Reference for the ESIA or ESMP , Questionnaires, list of stakeholders engaged, photographs, Aerial photographs or photos of significant environmental and social spots, as well as the credentials of the report authors and names presented.

## Slide 16
ANY QUESTIONS, COMMENTS AND REMARKS?

## Slide 17
THANK YOU FOR YOUR PATIENCE